Re-opening Requirements for Food Establishments after

Water Service Disruption or Contamination

Food establishments must not re-open until safe water service is restored and the local health department approves re-opening.

After safe water service has been restored, the following procedures should be completed prior to re-opening.  ALL PROCEDURES MUST BE COMPLETED WITH POTABLE WATER (water that is safe to drink).  POTABLE WATER MUST ALSO BE USED FOR HAND HYGIENE.

    - Flush all pipes and faucets.  Run both hot and cold water faucets for at least 5 minutes.

    - Thoroughly clean and sanitize all sinks before beginning to use them again.

    - Discard all ice in ice machines.

    - Flush, clean and sanitize all equipment connected to water lines according to the manufacturers’ instructions.  This equipment includes but is not limited to beverage-dispensing machines, ice machines, glass washers, dishwashers, spray misters, filters, coffee/tea urns, etc.

      - Contact your beverage distributor for post-mix machine cleaning instructions.

    - Run the empty dishwasher through the wash-rinse-sanitize cycle at least 3 times.  This will flush the water lines and ensure the dishwasher is cleaned and sanitized inside before washing dishes and utensils in it.

      - Consult manufacturer instructions or contact the product representative if further instructions are needed.

      - For chemical sanitizing machines, use approved test kit to ensure appropriate sanitizer strength has been reached.

      - For high temperature machines, the hot water temperature must reach 180°F.

    - After completing Step 4 above, use the dishwasher to wash and sanitize any dirty dishes.

    - Run water softeners through a generation cycle.

    - Flush drinking fountains by running water continuously for at least 5 minutes.

    - After completing the above procedures, notify your health inspector before resuming food operations.

For more information, please call the Lee County Health Department at 319-372-5225.